## Slide 1
IoT-Enabled Solar-Assisted
High-Efficiency Battery Charging
Using Supercapacitor Energy Buffering
Student:
Ajeesh Kumar R | 2024MT12104
Guide:
Dr. Somasundaram Iyyamperumal
Institution:
BITS Pilani WILP | Department of Engineering
Semester:
2, 2026 | Mid-Semester Viva
VIVA DATE
April 17, 2026
1 / 12

## Slide 2
INTRODUCTION
Background & Problem Statement
BACKGROUND
▸ Rising demand for efficient EV & battery charging infrastructure
▸ Solar PV integration offers sustainable energy but is inherently intermittent
▸ Direct solar-to-battery coupling causes voltage fluctuations & battery degradation
▸ Supercapacitors offer high power density & fast charge/discharge (>500K cycles)
▸ IoT enables real-time remote monitoring, diagnostics & data-driven optimization
PROBLEM STATEMENT
⚡
Grid voltage sags & fluctuations affect charger performance
☁️
Cloud cover causes rapid PV output variations (30–50% in seconds)
📊
No real-time monitoring in small-scale residential systems
🔧
Lack of adaptive control for changing input conditions
🌐
Absence of integrated IoT interface for remote data logging
💡 KEY INNOVATION
Combining supercapacitor buffering + STM32 embedded control + ESP8266 IoT monitoring in a unified, low-cost prototype
2 / 12

## Slide 3
INTRODUCTION
Objectives & Scope of Work
OBJECTIVES
1
Study conventional charging mechanisms & identify limitations in renewable energy contexts
2
Design solar-assisted smart charging system with supercapacitor energy buffering
3
Implement real-time monitoring & adaptive control using STM32 (ADC, PWM, UART)
4
Develop IoT edge gateway using ESP8266 for cloud connectivity & data visualization
5
Evaluate & compare charging performance metrics: efficiency, ripple, response time (buffered vs non-buffered)
✅ IN SCOPE
▸ Scaled low-voltage prototype (5–12V DC)
▸ STM32 + ESP8266 firmware development
▸ Cloud dashboard for real-time visualization
▸ Experimental: buffered vs non-buffered analysis
❌ OUT OF SCOPE
▸ Large-scale grid / high-voltage EV charging
▸ Custom PCB design (breadboard only)
▸ ML/AI-based optimization (future work)
▸ Multi-battery management systems
3 / 12

## Slide 4
LITERATURE REVIEW
Literature Review — Thematic Overview
☀️
Solar Charging Systems
▸ PV output varies 30–50% in seconds
▸ MPPT algorithms (P&O, IC) extract max power
▸ Doesn't address energy buffer problem
🔋
Supercapacitor Technology
▸ Power density: 1–10 kW/kg
▸ Cycle life: > 500,000 cycles
▸ Charge time: seconds to minutes
⚙️
Hybrid Energy Storage (HBSC)
▸ Passive / Semi-active / Active topologies
▸ Semi-active: best cost-performance ratio
▸ This project adopts semi-active design
🌐
IoT in Energy Management
▸ Remote monitoring & diagnostics
▸ Data-driven optimization
▸ ESP8266/ESP32: de-facto IoT standard
CONCLUSION: Supercapacitors ideal for transient absorption; batteries for sustained energy. Combining both + IoT = optimal solution.
4 / 12

## Slide 5
LITERATURE REVIEW
Key Papers & Research Gaps
Reference
Focus
Key Finding
Gap Identified
[1] Hassan et al., 2022
PV/Supercap energy systems analysis
Semi-active topology improves utilization 15–25%
No small-scale embedded prototype
[2] Zhang, 2023
Supercaps for renewable energy review
Reduces battery current ripple 40–70%
No real-time embedded control
[3] Gopi et al., 2024
HBSC systems for solar – review
Gap in IoT-enabled small-scale HBSC prototypes
No IoT integration
[4] Piyumal et al., 2021
Supercap-assisted hybrid PV
22% improvement in energy delivery efficiency
No IoT or remote monitoring
[5] Baqar et al., 2023
Supercap ageing in EV charging
35% extension of useful life via SoC control
Simulation-only, no IoT
→ THIS PROJECT ADDRESSES ALL IDENTIFIED GAPS
Integrated IoT monitoring • Real-time embedded control • Buffered vs non-buffered comparison • Automated cloud data logging
5 / 12

## Slide 6
RESEARCH METHODOLOGY
Research Methodology & Development Phases
METHODOLOGY APPROACH
▸ Modular hardware + software co-design approach
▸ Iterative development: design → implement → test → refine
▸ Experimental validation: buffered vs non-buffered comparison
▸ Three-part validation strategy:
▸ 1. Software simulation with realistic models
▸ 2. Hardware testing with regulated DC as solar simulator
▸ 3. Comparative analysis of charging metrics
▸ Semi-active HBSC topology (supercap via DC-DC converter)
▸ Closed-loop PI control for PWM regulation
✅
Phase 1
Design & Planning
Feb 2026
🔄
Phase 2
Hardware Setup
Mar 2026
🔄
Phase 3
Firmware Development
Mar–Apr 2026
📅
Phase 4
IoT Integration
Apr 2026
📅
Phase 5
Testing & Validation
Apr–May 2026
📅
Phase 6
Final Documentation
May 2026
6 / 12

## Slide 7
RESEARCH METHODOLOGY
System Architecture & Component Design
DC Power Supply
(5V–12V Solar Sim)
DC-DC Converter
(PWM Controlled)
Supercapacitor
(Energy Buffer)
Battery / Load
(Charging Target)
STM32F446RE — SENSING & CONTROL
▸ ADC: Voltage & current sensing (12-bit, 1 kHz, DMA)
▸ PWM: DC-DC converter control (TIM1, 20 kHz)
▸ Computation: P=V×I, Energy integration, SoC tracking
▸ Protection: 3-level hierarchy (Warning → Soft → Hard fault)
ESP8266 + CLOUD — IoT LAYER
▸ UART reception of JSON data from STM32 @ 115200 baud
▸ WiFi gateway → HTTP REST to cloud backend
▸ React.js dashboard with real-time Chart.js visualization
▸ Local SPIFFS buffering when offline
KEY COMPONENTS
▪ STM32F446RE Nucleo
Central Processing
▪ ESP8266 NodeMCU
WiFi IoT Gateway
▪ DC-DC Buck/Boost
Voltage Regulation
▪ Supercap 2.7V/10-100F
Energy Buffering
▪ ACS712 / INA219
Current Sensing
7 / 12

## Slide 8
DATA COLLECTION
Data Collection Plan & Current Progress
DATA COLLECTION STRATEGY
Parameter
Rate
Method
Input Voltage
1 kHz
STM32 ADC + DMA
Input Current
1 kHz
STM32 ADC + DMA
Supercap Voltage
1 kHz
STM32 ADC + DMA
Battery Voltage
100 Hz
Polled ADC
Cloud Transmission
1 Hz
UART → ESP8266 → WiFi
SAMPLE IoT DATA PACKET (JSON)
{ "voltage_in": 11.45, "current_in": 1.23, "power_in": 14.08, "efficiency_pct": 69.3, "supercap_soc_pct": 85.2, "system_state": "CHARGING" }
CURRENT PROGRESS
✅ System architecture finalized
✅ All components selected & sourced
✅ Computation methodology documented
✅ Literature review completed (5 papers)
✅ Repository structure established
✅ Cloud dashboard design completed
🔄 STM32 firmware: ADC & PWM modules
🔄 Hardware integration on breadboard
📅 ESP8266 IoT gateway integration
📅 End-to-end testing & data logging
📅 Buffered vs non-buffered experiments
8 / 12

## Slide 9
COMPUTATIONAL METRICS
📌 FACULTY FEEDBACK FOCUS
Computational Metrics — What & Why
WHAT ARE COMPUTATIONAL METRICS?
Computational metrics are quantitative measurements derived from mathematical formulas that characterize the performance, efficiency, and behaviour of the charging system. They transform raw sensor data (voltage, current) into meaningful engineering parameters that enable real-time decision making, closed-loop control, and experimental validation.
WHY ARE THEY NEEDED?
▸ Enable real-time system monitoring & feedback control
▸ Quantify charging performance (efficiency, power, energy)
▸ Drive closed-loop PWM regulation for optimal charging
▸ Provide comparative data: buffered vs non-buffered
▸ Ensure safety via protection threshold calculations
⚡
Power
P = V × I
Instantaneous power from
voltage × current (Watts)
🔋
Energy
E = Σ(P × Δt)
Cumulative energy over time
in Watt-hours
📈
Efficiency
η = P_out/P_in × 100%
Ratio of useful output
to total input power
🔌
Supercap SoC
SoC = (V²-V²min)/(V²max-V²min)
Energy-based state of charge
(proportional to V²)
⚙️
PWM Duty Cycle
D = V_out/V_in × 100%
Controls DC-DC converter
output voltage level
📊
Error Analysis
±2.06% total error
ADC quantization + sensor
accuracy combined
9 / 12

## Slide 10
COMPUTATIONAL METRICS
📌 FACULTY FEEDBACK FOCUS
Key Formulas & Practical Application
1. POWER CALCULATION
P = V × I
Example: V=12V, I=3A → P = 36W
STM32 computes this every 1ms from ADC readings. If solar panel outputs 12V at 3A, system delivers 36W.
2. ENERGY INTEGRATION
E[n] = E[n-1] + P[n] × Δt
Example: 36W × 5h = 180 Wh
Cumulative energy tracked in real-time. Δt = 1ms at 1kHz sampling. Converted to Wh by ÷3600.
3. SUPERCAPACITOR ENERGY
E = ½ × C × V²
Example: C=100F, V=2.7V → E = 364.5 J
Energy stored in supercap is proportional to V². This drives the SoC formula: SoC ∝ V².
4. CHARGING EFFICIENCY
η = (P_out / P_in) × 100%
Example: P_out=30W, P_in=36W → η = 83.3%
Key comparison metric. Expected: buffered system achieves 15–25% higher efficiency than non-buffered.
REAL-WORLD CHARGING SCENARIO — HOW METRICS WORK TOGETHER
1
SENSE
ADC reads V=11.5V,
I=1.23A every 1ms
2
COMPUTE
P = 11.5 × 1.23
= 14.15W
3
INTEGRATE
E += 14.15W × 0.001s
= 0.01415 J
4
CONTROL
PI controller adjusts
PWM duty cycle
5
PROTECT
Check V, I against
safety thresholds
6
TRANSMIT
JSON packet to ESP8266
→ Cloud dashboard
⏱ COMPLETE CYCLE TIME: < 10ms | SAMPLING: 1 kHz (1000 readings/sec) | CLOUD UPDATE: 1 Hz | MEASUREMENT ERROR: ±2.06%
10 / 12

## Slide 11
EXPECTED OUTCOMES
Expected Outcomes & Challenges
EXPECTED DELIVERABLES
🔧
STM32 Firmware
Sensor reading, PWM control, power calculation, UART comms
🌐
ESP8266 IoT Gateway
WiFi connectivity, cloud data transmission, local buffering
📊
Cloud Dashboard
Real-time charts, historical trends, system status via React.js
📄
Technical Documentation
Architecture, design rationale, computation methodology
🧪
Experimental Results
Buffered vs non-buffered performance analysis
💻
GitHub Repository
Full source code, data logs, and documentation
📋
Project Report
Academic report with complete analysis & conclusions
CHALLENGES & MITIGATIONS
⚠
Stable PWM control within 10ms budget
→ DMA for ADC & UART (non-blocking)
⚠
Component availability
→ Standard IoT modules (Nucleo, NodeMCU)
⚠
Noise in ADC measurements
→ Moving avg filter + RC low-pass (f_c=16kHz)
⚠
Cloud connectivity in lab
→ ESP8266 WiFi + SPIFFS offline buffer
⚠
System complexity
→ Modular architecture with clear interfaces
SIMULATION APPROACH
Python + NumPy + Matplotlib simulation for validation before hardware testing
11 / 12

## Slide 12
REFERENCES
References & Conclusion
REFERENCES
[1] Q. Hassan et al., "An analysis of photovoltaic/supercapacitor energy systems," Renewable Energy Reports, 2022.
[2] J. Zhang, "Supercapacitors for renewable energy applications: A review," Renewable and Sustainable Energy Reviews, 2023.
[3] C. V. V. M. Gopi et al., "Review of battery–supercapacitor hybrid energy storage systems for solar energy applications," Energy Reports, 2024.
[4] K. Piyumal et al., "Supercapacitor assisted hybrid PV systems for efficient energy management," Electronics, MDPI, 2021.
[5] M. Baqar et al., "Supercapacitor ageing control in residential microgrid based EV charging systems," Energies, MDPI, 2023.
🙏
THANK YOU
Questions & Discussion
Ajeesh Kumar R
2024MT12104
BITS Pilani WILP
github.com/2024mt12104/IoT-Solar-Charging-System
FUTURE SCOPE:
ML-based optimization • Multi-battery management • Custom PCB design • Grid-scale integration • Mobile app monitoring
12 / 12